## Slide 1: A Hybrid Approach for Fast and Accurate Trace Signal Selection for Post-Silicon Debug
Min Li and Azadeh Davoodi
Department of Electrical and Computer Engineering
University of Wisconsin-Madison
WISCAD Electronic Design Automation Lab http://wiscad.ece.wisc.edu/

## Slide 2: Comparison of Verification Methods
Approach | Throughput (Hz)
System simulation | ~103
RTL simulation | 101 to 103
Gate simulation | 10-1 to 101
Emulation | ~105
FPGA prototyping | ~106
Silicon | 107 to 109
Simulation is too slow!
  4-8 orders of magnitude slower than silicon
  e.g., for Pentium IV: 2 years of simulation = 2 min operation
[Table from Aitken, et al DAC’10]

## Slide 3: Post-Silicon Debug
Post-Silicon Debug (PSD) stage
  Stage after the initial chip tape-out and before the final release of product
Involves finding errors causing malfunctions
  Bugs found using real-time operation of a few manufactured chips with real-world stimulus
  Bugs fixed through multiple rounds of silicon steppings
Has become significantly expensive and challenging
  Mainly due to poor visibility of the internal signals inside the chips

## Slide 4: Embedded Logic Analyzer (ELA)
Control Unit
Trigger Unit
Sampling
Unit
Offload Unit
Assertion Checker
Trace Buffer
Trigger signals
Trigger condition
Traced data
Off-chip analysis
Assertion flags
Synchronization data
Trace signals
On-chip ELA
Used to increase visibility to internal signals
Captures the values of a few flipflops (i.e., trace signals) real-time and stores them inside the Trace Buffer
The traced data are then extracted off-chip and analyzed to restore the remaining signals inside the chip as many as possible

## Slide 5: Overview of Trace Buffer
Due to the limited on-chip area, the size of trace buffer is small
  e.g., B : 8 to 32 signals and M: 1K to 8K cycles
Terminology
  “Capture window” has a size of BxM
  “Observation window” has a size of BxN where N << M
Trace buffer is an on-chip buffer of size BxM
  B is the buffer bandwidth and identifies the number of signals which can be traced
  M is the depth of buffer and is equal to the number of clock cycles that tracing is applied
Cycle 0, 1 ….M-1
…
…
B
M
…
1
0
0
1

## Slide 6: Restoration Using Trace Signals
Restoration using “X-Simulation”
  At each cycle of the capture window, forward and backward restoration steps are applied iteratively until no more signals can be restored
DFF\Cycle | 0 | 1 | 2 | 3
F1 | X | X | X | X
F2 | 0 | 1 | 1 | 0
F3 | X | X | X | X
F4 | X | X | X | X
F5 | X | X | X | X
1 | 1 | 0 | X
X | 1 | 1 | X
X | 0 | X | X
Forward
Restoration
0
0
Backward
Restoration
0
0
Traced flipflop
f1
f2
f4
f5
f3

## Slide 7: Restoration Using Traced Signals
Quality of restoration is measured by the State Restoration Ratio (SRR)
  Measured within a capture window (BxM)
    Reflects the amount of restoration per trace signal per clock cycle
DFF\Cycle | 0 | 1 | 2 | 3
F1 | 1 | 1 | 0 | X
F2 | 0 | 1 | 1 | 0
F3 | X | 1 | 1 | X
F4 | X | X | X | X
F5 | X | 0 | X | X
Restored signal

## Slide 8: Trace Signal Selection Problem
  Challenges of PSD using trace buffers
    Due to the small trace buffer size, the capture window is small
      Different selections of the B trace signals can result in significantly different SRR
  Trace signal selection problem
  Given a trace buffer of size BxM
    Select B flipflops for tracing such that the remaining internal signals can be restored as many as possible during M cycles corresponding to the capture window
    Maximize the State Restoration Ratio (SRR)

## Slide 9: Existing Trace Selection Algorithms
Select one trace that leads to the largest SRR in each iteration
Selected B traces?
Terminate
Yes
No
Empty trace set
Forward Greedy
Prune one trace that leads to the smallest SRR in each iteration
B traces left?
Terminate
Yes
No
All traces
included
Backward Pruning
    Ko & Nicolici [DATE’08]
    Liu & Xu [DATE’09]
    Prabhakar & Xiao [ATS’09]
    Basu & Mishra [VLSI’11]
    Chatterjee & Bertacco [ICCAD’11]

## Slide 10: Existing Trace Selection Algorithms
Also categorized based on the way SRR is approximated
Metric-based
  Uses quick metrics to approximate SRR with high error but fast runtime
    Ko & Nicolici [DATE’08]
    Liu & Xu [DATE’09]
    Prabhakar & Xiao [ATS’09]
    Basu & Mishra [VLSI’11]
    Davoodi & Shojaei [ICCAD’10]
Simulation-based
  Uses X-Simulation to measure SRR accurately with backward pruning-travesal but still with a very long runtime
    Chatterjee & Bertacco [ICCAD’11]

## Slide 11: Simulation-Based Trace Selection
Much more accurate than metric-based
  Simulation can directly consider signal correlations
  Simulation accounts for the fact that a flipflop may be restored to different values within the observation window
Much slower than metric-based
  Restoration of each gate is evaluated using X-Simulation for each clock cycle
DFF\Cycle | 0 | 1 | 2 | 3
F1 | X | X | X | X
F2 | 0 | 1 | 1 | 0
F3 | X | X | X | X
F4 | X | X | X | X
F5 | X | X | X | X
1 | 1 | 0 | X
X | 1 | 1 | X
X | 0 | X | X

## Slide 12: Contributions
A hybrid trace signal selection algorithm
  Blend of simulation and metrics
  We propose a new set of metrics to quickly find a small number of top trace signal candidates at each step of the algorithm
  Next, among the few top candidates, X-Simulation is used to accurately evaluate the SRR and select the best
  We show our method has same or better solution quality compared to simulation-based approach with runtime as fast as the metric-based approaches

## Slide 13: Overview of Our Algorithm
Based on forward-greedy trace signal selection
Proposed metrics
  Reachability List of a flipflop f
    A small subset of flipflops which are good candidates to be restored by f
  Restorability Rate
    Rate that each flipflop is restored using the trace signals selected so far
  Restoration Demand of flipflop i from flipflop f
    Where flipflop f is candidate for the next trace signal
  Impact Weight of flipflop f
    How much f can restore the untraced flipflops after accounting for restoration from the already-selected trace signals
Initialize metrics
Compute fast metrics to
find a small number of top candidates for tracing
Selected B traces?
Terminate
No
Yes
Update metrics
Use a small number of X-Simulation to identify the best candidate (next trace) from the top candidates

## Slide 14: “Reachability List”
: Reachability list of flipflop f taking value v
  Defined for all flipflops f and values v = {0,1}
  A set of the flipflops which can be restored by f taking value v (without the help of any other flipflop)
  When evaluating how much a candidate trace signal f can restore other flipflops, only the elements in are considered
    Helps significantly reduce the algorithm runtime
    Computed once as a pre-processing step before the selection starts
f1
f2
f4
f5
f3

## Slide 15: “Restorability Rate”
: restorability rate of flipflop f
  Defined for any untraced flipflop f at each iteration
  Probability that f can be restored using the trace signals identified so far
Requires only one round of X-Simulation within a small observation window
  To compute for all untraced flipflops*
  * See Algorithm 3 in the paper for details
DFF\Cycle | 0 | 1 | 2 | 3
F1 | 1 | 1 | 0 | X
F2 | 0 | 1 | 1 | 0
F3 | X | 1 | 1 | X
F4 | X | X | X | X
F5 | X | 0 | X | X

## Slide 16: “Restoration Demand”
Restoration demand of flipflip i from flipflop f
  i should be in the reachability list of f
  the “remaining” restoration demand
  : probability that f takes values v
    The maximum f can offer to restore i
This expression is just an upper-bound approximation of the actual demand however it can be evaluated very quickly!
f1
f2
f4
f5
f3
Potentially-traced

## Slide 17: “Impact Weight”
  Defined for any untraced flipflop f
At each iteration of our algorithm, among the untraced flipflops, the ones with the highest impact weights are selected as the top candidates
  Top candidates set to only 5% of the number of flipflops
= + + +
f1
f2
f4
f5
f3

## Slide 18: Trace Selection Process
Method (i): At each iteration
  Identify top candidates using Impact Weights
  Select next trace from the top candidates using a small number of X-Simulations
Method (ii): After every 8 selected traces, consider adding an “island” flipflop
  Flipflop f is an island type if = =
Initialize metrics
Select next trace signal
Selected B traces?
Terminate
No
Yes
Method (i) Select using Impact Weights
Method (ii) Consider adding an “island” signal
Selected 8X traces?
No
Yes
Update metrics
    Island flipflops will never be selected as a trace signal using Method (i)
Use X-Simulation to measure SRR to identify the best island
  Few simulations because the number of islands are small (17% of the flipflops for S5378)

## Slide 19: Simulation Setup
Evaluation metric
  Use SRR to measure the restoration quality
  Experimented with trace buffers of size (8, 16, 32) X 4K cycles
Comparison made with
  METR: Metric-based: [Shojaei et al, ICCAD’10]
    Mainly used for runtime comparison
    Best reported runtime
  SIM: Simulation-based: [Chatterjee et al, ICCAD’11]
    Mainly used to compare solution quality
    Best reported solution quality

## Slide 20: Comparison of Runtime
Circuit | #DFF | #Traces | METR (sec) | SIM* (hr:min:sec) | Ours (sec)
S5378 | 163 | 8 | 8 | 00:06:50 | 5
 |  | 16 | 27 | 00:06:40 | 27
 |  | 32 | 66 | 00:05:30 | 28
S9234 | 145 | 8 | 6 | 00:07:28 | 26
 |  | 16 | 17 | 00:06:05 | 84
 |  | 32 | 38 | 00:04:10 | 86
S35932 | 1728 | 8 | 73 | 07:13:00 | 139
 |  | 16 | 167 | 07:12:00 | 208
 |  | 32 | 408 | 07:11:00 | 217
S38417 | 1564 | 8 | 3690 | 50:05:00 | 434 (8X faster)
 |  | 16 | 7620 | 50:04:00 | 2508 (3X faster)
 |  | 32 | 13428 | 50:02:00 | 2521 (5X faster)
S38584 | 1166 | 8 | 53 | 16:33:00 | 167
 |  | 16 | 140 | 16:32:00 | 741
 |  | 32 | 354 | 16:31:00 | 752
SIM significantly slower than METR and Ours
Ours has comparable or faster runtime than METR
* SIM ran on a quad-core machine using up to 8 threads

## Slide 21: Comparison of Solution Quality I
Circuit | #Traces | SRR METR | SRR SIM | SRR Ours | Improvement
S5378 | 8 | 13.7 | 12.8 | 13.6 | +6.3%
 | 16 | 8.1 | 7.1 | 8.0 | +12.7%
 | 32 | 4.1 | 4.4 | 4.2 | -4.5%
S9234 | 8 | 8.4 | 9.1 | 9.8 | +4.3%
 | 16 | 5.8 | 6.6 | 6.8 | +3.0%
 | 32 | 3.4 | 3.6 | 3.6 | +0.0%
S35932 | 8 | 31.1 | 58.1 | 61.4 | +5.7%
 | 16 | 19.4 | 36.2 | 38.3 | +5.8%
 | 32 | 11.6 | 23.1 | 23.4 | +1.3%
S38417 | 8 | 17.6 | 29.4 | 51.4 | +74.5%
 | 16 | 13.1 | 17.8 | 30.1 | +12.9%
 | 32 | 9.7 | 20.0 | 17.5 | -12.5%
S38584 | 8 | 13.5 | 14.9 | 24.0 | +31.1%
 | 16 | 10.8 | 18.1 | 18.5 | +2.2%
 | 32 | 7.1 | 16.4 | 17.5 | +6.7%
Average |  |  |  |  | 10.0%
On average 10.0% improvement in SRR compared to SIM
SIM typically has much higher SRR than METR, especially in larger benchmarks

## Slide 22: Identification using Impact Weights
Chart: Rate of correctly identified top candidates (for S38417)
% matched top candidates | 0.93 | 0.9 | 0.91 | 0.94 | 0.95 | 0.91 | 0.92 | 0.95
How accurate are the top candidates identified by Impact Weights?
  Use SRR to identify the “actual” top candidates (resulting in the highest SRR) by X-Simulation
    Used as the golden case
  Identify the top candidates obtained using Impact Weights which are also top candidates in the golden case

## Slide 23: Comparison of Solution Quality II
Circuit | #Traces | SRR Ours-w/o SIM | SRR Ours | Improvement
S5378 | 8 | 13.4 | 13.6 | -1.5%
 | 16 | 7.9 | 8.0 | -1.3%
 | 32 | 4.0 | 4.2 | -4.8%
S9234 | 8 | 9.4 | 9.8 | -4.1%
 | 16 | 6.1 | 6.8 | -10.3%
 | 32 | 3.3 | 3.6 | -8.3%
S35932 | 8 | 31.6 | 61.4 | -48.5%
 | 16 | 18.9 | 38.3 | -50.7%
 | 32 | 11.3 | 23.4 | -51.7%
S38417 | 8 | 18.1 | 51.4 | -64.8%
 | 16 | 10.3 | 30.1 | -65.8%
 | 32 | 5.9 | 17.5 | -66.3%
S38584 | 8 | 18.3 | 24.0 | -23.8%
 | 16 | 14.8 | 18.5 | -20.0%
 | 32 | 10.7 | 17.5 | -38.9%
Ours-w/o SIM: Our algorithm when the next trace is the candidate with highest Impact Weight
  X-Simulation is not used to find the best candidate
This experiment shows that X-Simulation is necessary

## Slide 24: Comparison of Solution Quality III
Circuit | #Traces | SRR Ours-w/o Islands | SRR Ours | Improvement
S5378 | 8 | 12.5 | 13.6 | -8.1%
 | 16 | 7.8 | 8.0 | -2.5%
 | 32 | 4.1 | 4.2 | -2.4%
S9234 | 8 | 8.1 | 9.8 | -17.3%
 | 16 | 6.5 | 6.8 | -4.4%
 | 32 | 3.5 | 3.6 | -2.8%
S35932 | 8 | 61.4 | 61.4 | +0.0%
 | 16 | 38.3 | 38.3 | +0.0%
 | 32 | 23.4 | 23.4 | +0.0%
S38417 | 8 | 48.2 | 51.4 | -6.2%
 | 16 | 28.7 | 30.1 | -4.7%
 | 32 | 16.7 | 17.5 | -4.6%
S38584 | 8 | 23.9 | 24.0 | -0.4%
 | 16 | 18.5 | 18.5 | +0.0%
 | 32 | 17.5 | 17.5 | +0.0%
Ours-w/o Islands: Our algorithm when 8X traces are selected
  Islands are not considered
This experiment shows that the solution quality of some benchmarks are influenced by the islands
  Islands tend to have a larger impact on smaller trace buffer widths

## Slide 25: Summary
We presented a new trace signal selection algorithm
  Utilizes a small number of simulations with quickly-evaluated metrics at each iteration
  Has comparable or better solution quality with respect to a simulation-based algorithm
  Has similar runtime to a metric-based algorithm

## Slide 26
Thank You!
Questions?
adavoodi@wisc.edu

## Slide 27: Simulation-based Approximation of SRR
Done using X-Simulation but for an “observation window” instead of the entire the capture window
  e.g., Chatterjee et al [ICCAD’11] shows the SRR computed for an observation window of 64 cycles is sufficiently close to the SRR corresponding to the capture window of 4K cycles
DFF\Cycle | 0 | 1
F1 | 1 | X
F2 | 0 | 1
F3 | X | 1
F4 | X | X
F5 | X | 0
observation window << capture window

## Slide 28: Metric-based Approximation of SRR
Example
  “Visibility” metric proposed by Liu, et al [DATE’09]
  Visibility of a flipflop represents how much it can be restored using the currently-selected trance signals
  Summation of visibility of all untraced flipflops is used as an estimate of SRR
Total Visibility = 2+1+1 = 4
Traced
f1
f2
f4
f5
f3

## Slide 29: Metric-based Approximation of SRR
Example metric
  “Visibility” Liu, et al [DATE’09]
  Two visibility metrics computed per gate output
    /: The probability that the value “0/1” is actually restored at the output of each gate
    Computed using iteratively traversing the circuit and updating the gate visibilities until convergence
  Total visibility is the summation of / over all the untraced flipflops
    Inaccurate approximation of SRR due to ignoring signal correlations
Traced
Visibility = 1+1+0.25+0.75+0.75+0.25 = 4
f1
f2
f4
f5
f3

## Slide 30: Comparison of Solution Quality IV
Circuit | #Traces | SRR Forward Greedy | SRR Ours | Improvement
S5378 | 8 | 13.5 | 13.6 | -0.7%
 | 16 | 7.9 | 8.0 | -1.3%
 | 32 | 4.2 | 4.2 | +0.0%
S9234 | 8 | 9.8 | 9.8 | +0.0%
 | 16 | 5.9 | 6.8 | -13.2%
 | 32 | 3.5 | 3.6 | -2.8%
S35932 | 8 | 59.3 | 61.4 | -3.4%
 | 16 | 37.4 | 38.3 | -2.3%
 | 32 | 22.3 | 23.4 | -4.7%
S38417 | 8 | 51.5 | 51.4 | +0.0%
 | 16 | 24.0 | 30.1 | -19.6%
 | 32 | 16.8 | 17.5 | -4.0%
S38584 | 8 | 25.1 | 24.0 | +4.6%
 | 16 | 20.7 | 18.5 | +11.9%
 | 32 | 18.0 | 17.5 | +2.9%
Forward greedy: Simulation combined with forward greedy selection strategy

## Slide 31: Distribution of Impact Weights
Chart: 
| top-k | rest | top-k | rest | top-k | rest
Avg Impact Weight | 22.38 | 0.37 | 22.36 | 0.48 | 12.98 | 0.43
Itr. 1
Itr. 2
Itr. 3
Observed after three iterations in benchmark S38417
  Impact Weights of top candidates are much higher than the remaining signals