## Slide 1: Trace Signal Selection for Post-Silicon Debug
WISCAD Electronic Design Automation Lab http://wiscad.ece.wisc.edu/

## Slide 2: Outline
A fast and high quality trace signal selection algorithm for multi-mode of operation
A fast and high quality trace signal selection algorithm for a single-mode of operation
Challenges of post-silicon debug
Post-silicon debug using trace buffers
The trace signal selection problem
Background and Preliminaries
Hybrid single-mode trace signal selection (SMTS)
Multi-mode trace signal selection (MMTS)
Preliminaries
Single-mode
Multi-mode
Hybrid single-mode trace signal selection (SMTS)
Multi-mode trace signal selection (MMTS)

## Slide 3: Post-Silicon Debug (PSD)
Real-time operation of a few manufactured chips with real-world stimulus
Involves finding errors causing malfunctions
  Fix through multiple rounds of Silicon Stepping/Revision
Has become significantly time-consuming and expensive
  Tight Time-to-Market requirement
  Formal verification and simulation tools do not scale as technology scales
  Poor visibility inside the chip
Control Signals
Prior Work
PSD Overview
Restoration using TB
Preliminaries
Single-mode
Multi-mode
Figure from Abramovici et al. [DAC’06]

## Slide 4: Overview of Techniques for PSD
Methods to increase visibility inside the chip during PSD:
Manual probing, e.g., Paniccia et al. [ITC’98]
Customized solutions for debugging microprocessors, e.g., Park et al. [DAC’08]
Recording the values of flipflops using:
  Traditional Design-for-Test (DFT) structures (e.g., scan chains)
  Trace buffer-based solutions (i.e., Embedded Logic Analyzer (ELA))
In pre-silicon every signal is observable
In post-silicon most internal signals become inaccessible
Preliminaries
Single-mode
Multi-mode
Control Signals
Prior Work
PSD Overview
Restoration using TB

## Slide 5: Debug using Trace Buffer
Use trace buffer technology
  Trace buffer is embedded inside a Circuit-under-Debug (CUD)
  Trigger an event in the CUD
  Real-time capture values of a few selected flipflops which are stored in on-chip buffers
  Extract and analyze
Figure from Yang et al. [DATE’09]
Preliminaries
Single-mode
Multi-mode
Control Signals
Prior Work
PSD Overview
Restoration using TB

## Slide 6: Trace Buffer as A Part of ELA
Control Unit
Trigger Unit
Sampling
Unit
Offload Unit
Assertion Checker
Trace Buffer
Trigger signals
Trigger condition
Traced data
Off-chip analysis
Assertion flags
Synchronization data
Trace signals
On-chip ELA captures the values of the trace signals during real-time operation and stores them inside the trace buffer which are then extracted off-chip and analyzed
Only a few flipflops could be selected beforehand as trace signals. They should be able to restore the values of the remaining signals inside the chip as much as possible
Preliminaries
Single-mode
Multi-mode
Control Signals
Prior Work
PSD Overview
Restoration using TB

## Slide 7: Overview of Trace Buffer
Trace buffer is an on-chip buffer of size BxM
  B is the buffer bandwidth and identifies the number of signals which can be traced
  M is the depth of buffer and is equal to the number of clock cycles when the trace signals are captured
M-1
…
…
M
B
…
1
0
0
1
“Capture window” has a size of BxM
“Observation window” has a size of BxN where N << M
Preliminaries
Single-mode
Multi-mode
…
…
Control Signals
Prior Work
PSD Overview
Restoration using TB

## Slide 8: Restoration using Trace Signals
Restoration using “X-Simulation”
  At each cycle of the capture window, forward and backward restoration steps are applied iteratively until no more signals can be restored
Forward
Restoration
0
0
Backward
Restoration
0
0
Traced flipflop
f1
f2
f4
f5
f3
DFF\Cycle | 0 | 1 | 2 | 3
F1 | 1 | 1 | 0 | X
F2 | 0 | 1 | 1 | 0
F3 | X | 1 | 1 | X
F4 | X | X | X | X
F5 | X | 0 | X | X
Preliminaries
Single-mode
Multi-mode
Control Signals
Prior Work
PSD Overview
Restoration using TB

## Slide 9: Restoration using Trace Signals
Quality of restoration is measured by the metric State Restoration Ratio (SRR)
  Measured within the capture window
  Widely used by Prabhakar & Xiao [ATS’09], Ko & Nicolici [TCAD’09], Chatterjee et al. [ICCAD’11], Liu & Xu [TCAD’12], Basu & Mishra [TVLSI’13] , etc.
Restored signal
DFF\Cycle | 0 | 1 | 2 | 3
F1 | 1 | 1 | 0 | X
F2 | 0 | 1 | 1 | 0
F3 | X | 1 | 1 | X
F4 | X | X | X | X
F5 | X | 0 | X | X
Preliminaries
Single-mode
Multi-mode
Control Signals
Prior Work
PSD Overview
Restoration using TB
Trace flipflop

## Slide 10: Trace Signal Selection Problem
  Challenges of PSD using trace buffers
    Due to limited on-chip white-spaces and memory, trace buffer size is small: trace buffer width (8~64 bits) and depth (1K~8K clock cycles)
    Different selections of the B trace signals can result in significantly different SRR
  Trace signal selection problem
  Given a trace buffer of size BxM
    Select B flipflops for tracing such that the remaining flipflops can be restored as many as possible during M cycles corresponding to the capture window
    Maximize the State Restoration Ratio (SRR)
Preliminaries
Single-mode
Multi-mode
Control Signals
Prior Work
PSD Overview
Restoration using TB

## Slide 11: Existing Trace Signal Selection Algorithms
Simulation-based
  Uses X-Simulation to measure SRR accurately but it results in a very long runtime
  Select trace signals in a backward greedy manner
    Chatterjee et al. [ICCAD’11]
Metric-based
  Uses metrics to approximate SRR with fast runtime but it results in high error
  Selects trace signals in a forward greedy manner
    Prabhakar & Xiao [ATS’09], Ko & Nicolici [TCAD’09], Liu & Xu [TCAD’12], Basu & Mishra [TVLSI’13]
Select one trace leading to the largest SRR in each iteration
B traces selected?
Terminate
Yes
No
Empty trace set
Prune one flipflop that leads to the smallest SRR in each iteration
B traces left?
Terminate
Yes
No
All flipflops included
Preliminaries
Single-mode
Multi-mode
Control Signals
Prior Work
PSD Overview
Restoration using TB

## Slide 12: Measuring SRR in Simulation-based Techniques
Uses X-Simulation to measure SRR accurately
Due to the long runtime, performed for an “observation window” smaller than the capture window
  e.g., Chatterjee et al. [ICCAD’11] shows that the SRR computed for an observation window of 64 cycles is sufficiently close to the SRR measured from a capture window of 4K cycles
DFF\Cycle | 0 | 1
F1 | 1 | X
F2 | 0 | 1
F3 | X | 1
F4 | X | X
F5 | X | 0
observation window << capture window
Preliminaries
Single-mode
Multi-mode
Control Signals
Prior Work
PSD Overview
Restoration using TB

## Slide 13: Metric-based Approximation of SRR
Example metric
  “Visibility” Liu, et al. [TCAD’12]
  Two visibility metrics computed per gate output
    /: The probability that the value “0/1” is restored at the output of each gate
    Computed using iteratively traversing and updating the gate visibilities until convergence
Trace flipflop
Visibility = 1+1+0.25+0.75+0.75+0.25 = 4
f1
f2
f4
f5
f3
Preliminaries
Single-mode
Multi-mode
  Total visibility is defined as the summation of / over all the untraced flipflops
    Inaccurate estimation of SRR due to ignoring signal correlations
    Does not capture cycle-to-cycle behavior
Control Signals
Prior Work
PSD Overview
Restoration using TB

## Slide 14: Comparison
Simulation-based much more accurate than metric-based
  Simulation can directly consider signal correlations
  Simulation accounts for the fact that a flipflop may be restored to different values within the observation window
Simulation-based much slower than metric-based
  Restoration of each gate is evaluated using X-Simulation for each clock cycle however in metric-based the “0/1” visibility per gate is computed once
DFF\Cycle | 0 | 1 | 2 | 3
F1 | 1 | 1 | 0 | X
F2 | 0 | 1 | 1 | 0
F3 | X | 1 | 1 | X
F4 | X | X | X | X
F5 | X | 0 | X | X
Preliminaries
Single-mode
Multi-mode
Control Signals
Prior Work
PSD Overview
Restoration using TB

## Slide 15: Impact of Control Signals
Control signals define different modes of operation
  For example, two control signals define four modes of operation including addition, subtraction, multiplication, division for an ALU
  control signals result up to number of modes
  Other examples: reset, mode selection, scan enable, power gating, decryption/encryption, communication between different design blocks etc.
Control signals can greatly impact the restoration process
  When c is “1”, the restoration is independent of , and when c is “0”, the restoration is independent of
  The amount of restoration is directly affected by the value of the control signal, regardless of which flipflops may be selected for tracing
f1
f3
f2
c
control signal
Preliminaries
Single-mode
Multi-mode
Control Signals
Prior Work
PSD Overview
Restoration using TB

## Slide 16: Considering Control Signals During Selection
Control signals have been considered during trace signal selection
  Values of control signals are randomly changed
    In previous work e.g. Ko & Nicolici [TCAD’09]
    Inaccurately shows high restoration e.g. when reset is activated but bugs are expected to happen when reset is deactivated
  Trace signals are selected for a single mode of operation
    It means to keep the control signals constant throughout the selection process to the values corresponding that mode of operation
    In various works including Chatterjee et al. [ICCAD’11], Liu & Xu [TCAD’12], Basu & Mishra [TVLSI’13], etc.
    May yield to poor restoration if a bug is observed in another mode of operation
Preliminaries
Single-mode
Multi-mode
Control Signals
Prior Work
PSD Overview
Restoration using TB

## Slide 17: Contributions
A hybrid trace signal selection algorithm for a single-mode of operation
  Uses a “right blend” of new metrics with a small number of X-Simulations during the trace signal selection
  Achieves a solution quality as good as simulation-based algorithms and runtime as fast as metric-based algorithms
Multi-mode trace signal selection algorithm
  Propose the trace signal selection problem when considering restoration over all the operation modes
  We show it achieves a much higher restoration over all the operation modes compared to other algorithms
Automated identification of control signals
  Propose a procedure to identify the control signals in a gate-level circuit
  Identified control signals are fed into the single-mode and multi-mode trace signal selection problems
Preliminaries
Single-mode
Multi-mode

## Slide 18: Outline
Preliminaries
Single-mode
Multi-mode
Background and Preliminaries
Hybrid single-mode trace signal selection (SMTS)
Multi-mode trace signal selection (MMTS)

## Slide 19: Overview of Our Framework
Method (i) uses a “forward-greedy” strategy to select the next trace signal guided by the metrics
Method (ii) uses a non-greedy selection strategy by adding the “island” flipflops
Preliminaries
Single-mode
Multi-mode
Simulation Results
Selection Process
Overview
Metrics
Initialize metrics
Select next trace signal
Selected B traces?
Terminate
No
Yes
Method (i) forward-greedy selection guided by metrics
Method (ii) Consider adding an “island” flipflops as the next trace signal
Selected 8X traces?
No
Yes
Update metrics

## Slide 20: Contributions
A new set of metrics are able to quickly find a small number of top trace signal candidates in order to select the best one as the next trace signal at each iteration of the algorithm
  After identifying the top candidates, a few number of X-Simulations are used to accurately evaluate the SRR and select the best
Metrics are computed fast
  Metrics that do not require any X-Simulation
    “Impact Weight” and “Restoration Demand”
  Metrics that require a small number of X-Simulations
    “Reachability List” and “Restorability Rate”
Preliminaries
Single-mode
Multi-mode
Simulation Results
Selection Process
Overview
Metrics

## Slide 21: “Reachability List”
: Reachability list of flipflop f taking value v
  Defined for a flipflop f when it takes value v = {0,1}
  A set of the flipflops which can be directly restored by f taking value v (without the help of any other flipflop)
Computed using X-Simulation
  As a pre-processing step before any signal is selected
  Very fast per flipflop
f1
f2
f4
f5
f3
Reachability List
Restorability Rate
Restoration Demand
Impact Weight
Preliminaries
Single-mode
Multi-mode
Simulation Results
Selection Process
Overview
Metrics

## Slide 22: “Restorability Rate”
: Restorability rate of flipflop f
  Computed for any untraced flipflop f at each iteration
  Defined as the probability that f can be restored using the trace signals selected so far
DFF\Cycle | 0 | 1 | 2 | 3
F1 | 1 | 1 | 0 | X
F2 | 0 | 1 | 1 | 0
F3 | X | 1 | 1 | X
F4 | X | X | X | X
F5 | X | 0 | X | X
Requires a small number of X-Simulations
  At each iteration, all values are computed using an observation window of 64 cycles instead of the entire capture window
Preliminaries
Single-mode
Multi-mode
Reachability List
Restorability Rate
Restoration Demand
Impact Weight
Simulation Results
Selection Process
Overview
Metrics

## Slide 23: “Restoration Demand”
: Demand of untraced flipflop i from trace-candidate flipflop f when f takes value v
  the amount that i needs to be fully restored
    : restorability rate using traces selected so far
  : probability that f takes value v
    Upper bound on restoration that f can offer to i
f1
f2
f4
f5
f3
Already-traced
Trace-signal-candidate
Preliminaries
Single-mode
Multi-mode
Reachability List
Restorability Rate
Restoration Demand
Impact Weight
Simulation Results
Selection Process
Overview
Metrics

## Slide 24: “Impact Weight”
  Defined for any trace-candidate flipflop f
= + + +
f1
f2
f4
f5
f3
At each iteration of our algorithm, impact weights are computed to identify a small number of top candidates
  Top candidate are the 5% with the highest impact weights
Trace-signal-candidate
Preliminaries
Single-mode
Multi-mode
Reachability List
Restorability Rate
Restoration Demand
Impact Weight
Simulation Results
Selection Process
Overview
Metrics

## Slide 25: Trace Signal Selection Process
Method (i): Select the next trace signal from the top candidates
  Use X-Simulation to measure SRR for each top candidate
  The next trace signal is the one with the highest SRR among the top candidates
Initialize metrics
Select the next trace signal
Selected B traces?
Terminate
No
Yes
Method (i) Select guided by impact weight
Method (ii) Consider adding an “island” flipflop
Selected 8X traces?
No
Yes
Update metrics
To accelerate the process
  Parallel execution of X-Simulation
  Incremental update of the metrics
Preliminaries
Single-mode
Multi-mode
Simulation Results
Selection Process
Overview
Metrics
  The number of X-Simulations is few

## Slide 26: Trace Signal Selection Process
Method (ii): After every 8 trace signals are selected, consider adding an “island” flipflop
  Flipflop f is an island type if = =
    These types of flipflops will never be selected using Method (i)
Use X-Simulation to measure SRR to identify the best island flipflop
  Few X-Simulations because the number of islands are small (17% of the flipflops for S5378)
Initialize metrics
Select the next trace signal
Selected B traces?
Terminate
No
Yes
Method (i) Select guided by impact weight
Method (ii) Consider adding an “island” flipflop
Selected 8X traces?
No
Yes
Update metrics
Preliminaries
Single-mode
Multi-mode
Simulation Results
Selection Process
Overview
Metrics

## Slide 27: Simulation Setup
Simulation Setup
  Use SRR to measure the restoration quality
  Experimented with trace buffers of size (8, 16, 32) X 4K
Comparison made with
  METR: Metric-based: Shojaei et al. [ICCAD’10]
    Mainly used for runtime comparison
    One of the best reported runtime
  SIM: Simulation-based: Chatterjee et al. [ICCAD’11]
    Mainly used to compare solution quality
    Best reported solution quality
  Other Metric-based:
    Liu & Xu [TCAD’12]
    Ko & Nicolici [TCAD’09]
    Basu & Mishra [TVLSI’13]
Preliminaries
Single-mode
Multi-mode
Simulation Results
Selection Process
Overview
Metrics

## Slide 28: Comparison of SRR
Circuit | #Traces | METR | SIM | Ours | Impr.-METR | Impr.-SIM
S5378 | 8 | 13.7 | 12.8 | 13.6 | -0.7% | +6.3%
 | 16 | 8.1 | 7.1 | 8.0 | -1.2% | +12.7%
 | 32 | 4.1 | 4.4 | 4.2 | +2.4% | -4.5%
S9234 | 8 | 8.4 | 9.1 | 9.8 | +16.7% | +4.3%
 | 16 | 5.8 | 6.6 | 6.8 | +17.2% | +3.0%
 | 32 | 3.4 | 3.6 | 3.6 | +5.9% | +0.0%
S35932 | 8 | 31.1 | 58.1 | 61.4 | +97.4% | +5.7%
 | 16 | 19.4 | 36.2 | 38.3 | +97.4% | +5.8%
 | 32 | 11.6 | 23.1 | 23.4 | +101.7% | +1.3%
S38417 | 8 | 17.6 | 29.4 | 51.4 | +192.0% | +74.5%
 | 16 | 13.1 | 17.8 | 30.1 | +129.8% | +12.9%
 | 32 | 9.7 | 20.0 | 17.5 | +80.4% | -12.5%
S38584 | 8 | 13.5 | 14.9 | 24.0 | +77.8% | +31.1%
 | 16 | 10.8 | 18.1 | 18.5 | +71.3% | +2.2%
 | 32 | 7.1 | 16.4 | 17.5 | +146.5% | +6.7%
Avg. |  |  |  |  | +69.0% | 10.0%
Preliminaries
Single-mode
Multi-mode
Simulation Results
Selection Process
Overview
Metrics

## Slide 29: Comparison of Runtime
Circuit | #DFF | #Traces | METR (sec) | SIM* (hr:min:sec) | Ours (sec) | Impr.METR(sec)
S5378 | 163 | 8 | 8 | 00:06:50 | 5 | +3
 |  | 16 | 27 | 00:06:40 | 27 | 0
 |  | 32 | 66 | 00:05:30 | 28 | +38
S9234 | 145 | 8 | 6 | 00:07:28 | 26 | -20
 |  | 16 | 17 | 00:06:05 | 84 | -67
 |  | 32 | 38 | 00:04:10 | 86 | -48
S35932 | 1728 | 8 | 73 | 07:13:00 | 139 | -66
 |  | 16 | 167 | 07:12:00 | 208 | -41
 |  | 32 | 408 | 07:11:00 | 217 | +191
S38417 | 1564 | 8 | 3690 | 50:05:00 | 434 | +3255(8X)
 |  | 16 | 7620 | 50:04:00 | 2508 | +5112(3X)
 |  | 32 | 13428 | 50:02:00 | 2521 | +10907(5X)
S38584 | 1166 | 8 | 53 | 16:33:00 | 167 | -114
 |  | 16 | 140 | 16:32:00 | 741 | -601
 |  | 32 | 354 | 16:31:00 | 752 | -389
* Ran SIM on a quad-core machine using up to 8 threads
Preliminaries
Single-mode
Multi-mode
Simulation Results
Selection Process
Overview
Metrics

## Slide 30: Comparison with Other Metric-based Algorithms
Compared separately because the control signals are set differently from one to another
  Liu & Xu [TCAD’12]
    Ours has a significant SRR improvement of on average 136.02%
  Ko & Nicolici [TCAD’09]
    Ours has a significant SRR improvement of on average 105.32%
  Basu & Mishra [TVLSI’13]
    Ours has an SRR improvement of on average 6.5%
    Runtimes of our approach are much better as Basu & Mishra runs almost 5X longer on average
Preliminaries
Single-mode
Multi-mode
Simulation Results
Selection Process
Overview
Metrics

## Slide 31: Identifying the Top Candidates
Report the Impact Weights in three iterations of S38417
  Impact Weights of the top candidates close to each other
  Impact Weights of the remaining signals much lower than the top candidates
  Therefore, Impact Weight is able to identify the top candidates
Chart: 
| top-5% | rest | top-5% | rest | top-5% | rest
Avg Impact Weight | 22.38 | 0.37 | 22.36 | 0.48 | 12.98 | 0.43
Itr. 1
Itr. 2
Itr. 3
67.8
3.7
44.5
9.0
31.6
4.0
3.0
8.0
4.0
Preliminaries
Single-mode
Multi-mode
Simulation Results
Selection Process
Overview
Metrics

## Slide 32: Summary
We presented a hybrid trace signal selection algorithm
  Utilized a small number of X-Simulations with quickly-evaluated metrics at each iteration
  Had comparable or better solution quality
    Compared to a simulation-based algorithm which had the best reported solution quality
  Had similar runtime to a metric-based algorithm
    Which had one of the fastest runtimes
Our algorithm considered a single mode of operation
  For example for benchmark S35932 with 4 different modes of operation
    We solve the SMTS problem for each mode and we measure the solution quality separately and report the average SRR value of all the modes
  Next, we discuss the multi-mode trace signal selection problem
Preliminaries
Single-mode
Multi-mode

## Slide 33: Outline
A trace signal selection algorithm
  Maximizes the restoration over all the operation modes
  Avoids a purely greedy selection strategy
  Has a better solution quality than various algorithms
Preliminaries
Single-mode
Multi-mode
Background and Preliminaries
Hybrid single-mode trace signal selection (SMTS)
Multi-mode trace signal selection (MMTS)

## Slide 34: Motivation for Multi-Mode Trace Signal Selection
 | 17.0 | 4.3
 | 14.3 | 8.2
 | 17.0 | 4.3
 | 14.3 | 8.2
    Case study of S38584
Observations
  SRR of SMTS solution in each mode is higher in that mode
    For example, obtained from is almost doubled in mode 1 than obtained from
    This can be a problem during the debugging process since the operation mode when a bug occurs is not a-priori known
  Therefore it is important to consider all the operation modes during the selection process
      For each solution evaluated the SRR for modes 0 and 1
      Ran our single mode trace selection procedure for two different modes of operation
Preliminaries
Single-mode
Multi-mode
Simulation Results
Algorithm
MMTS
Mode Merging
        : trace signals selected when g35 is “0” throughout the selection process
        : trace signals selected when g35 is “1” throughout the selection process

## Slide 35: Contributions
Extending the problem definition when considering multiple modes
Mode Merging
  A procedure to reduce the number of modes by merging the modes with “similar restoration maps”
Algorithm
  A procedure based on perturbing an initial single-mode optimized solution (selected from a suitable “start” mode) to improve the restorability over all the modes
  Our algorithm can finish in reasonable runtime with solution quality close to a reference case which defines an upper bound on the best attainable solution quality
Preliminaries
Single-mode
Multi-mode

## Slide 36: Multi-mode Trace Signal Selection Problem
Multi-mode Trace Signal Selection problem (MMTS)
  Given a trace buffer of size , and a set of control signals defining operation modes, the Multi-mode Trace Signal Selection problem selects flipflops, in order to maximize MSRR over a debugging window of N cycles
  Multi-mode State Restoration Ratio (MSRR)
    Defined as summation of State Restoration Ratios (SRRs) of different modes obtained from a given set of selected trace signals
Preliminaries
Single-mode
Multi-mode
Simulation Results
Algorithm
MMTS
Mode Merging

## Slide 37: Mode Merging: Motivation
Restoration map for S35932
  Two control signals are set to four values corresponding to four operation modes
  Four restoration maps are generated when no trace signal is selected yet
Observations
  There are modes with similar restoration maps and can be merged into a single mode
  In this case, modes 0 and 1 can be merged, so are modes 2 and 3
In each restoration map
  Green pixel: gate restored to 0
  Black pixel: gate restored to 1
  Red pixel: unrestored gate
Preliminaries
Single-mode
Multi-mode
Simulation Results
Algorithm
MMTS
Mode Merging

## Slide 38: Mode Merging: Procedure
Merging two modes
  Once two modes are merged, they are considered as one mode
  The values of the control signals will correspond to the values of one of the merged modes
  The rest of the modes are merged in the same way until no modes can be merged
Consider two modes and
Measure the number of restored gates ( and ) for each mode
?
Y
Merge the two modes into one
Count the number of common gates in and denoted by
Compute similarity ratio
Preliminaries
Single-mode
Multi-mode
Simulation Results
Algorithm
MMTS
Mode Merging

## Slide 39: IteM: Iterative Multi-mode Trace Signal Selection
Overview of our procedure:
Identify a suitable start mode
  Compute a set representing the union of the reachability lists of all the flipflops in that mode
  Pick the one with the largest set size among all modes of operation
  Generate an initial solution using our single mode algorithm
Iteratively perturb the current solution to improve restoration over all the modes
  Swap up to trace signals at each iteration
Terminate when no improvement in MSSR in 20 consecutive iterations
Generate an initial solution
Termination
20 itr. W/O improvement?
Iteratively perturb the solution
Yes
No
Preliminaries
Single-mode
Multi-mode
Find
Simulation Results
Algorithm
MMTS
Mode Merging

## Slide 40: Overview of Swap in One Iteration
Swap r signals
r > R
?
DONE
Set swap to DET (deterministic);
radius
START
Swap is DET ?
Set swap to RAND
(random);
radius
Accept
?
r++
N
N
Y
Y
N
Y
swap RAND
r=1 signal
Initially perform swap in a deterministic mode with radius gradually increased to ()
  Exit the loop whenever a solution is accepted
A solution is accepted
  When there is an improvement in MSRR
  Uses a probabilistic acceptance criteria to probabilistically accept the swap when there is no improvement in MSRR
If no solution is accepted when , repeat with random swap
Preliminaries
Single-mode
Multi-mode
Simulation Results
Algorithm
MMTS
Mode Merging

## Slide 41: Features of Our Swapping Procedure
Swapping procedure is non-greedy
  Perturbation radius is gradually increased in each iteration
    Makes small perturbation around the current solution
    Allows not getting trapped in local minima by gradually increasing the radius
  Probabilistic acceptance criteria
    Similar to simulated annealing
    Allows exploring the search space and accepting bad solutions
Simulation Results
Algorithm
MMTS
Mode Merging
Preliminaries
Single-mode
Multi-mode

## Slide 42: Swapping r Trace Signals
Eliminating r trace signals which are least promising
  Deterministic (DET) elimination:
    Uses X-Simulations to evaluate the MSRR of currently-selected trace signals
    Eliminates r trace signals leading to the least MSRR
  Random (RAND) elimination:
    Randomly eliminates r trace signals
Adding r most promising trace signals
  Performed deterministically (both DET and RAND swaps)
  Similar to our single-mode algorithm
    Identifies the top candidates using multi-mode restoration metric , which I will discuss in the next slide
    Uses X-Simulation to pick the r signals with the highest MSRR
Preliminaries
Single-mode
Multi-mode
Simulation Results
Algorithm
MMTS
Mode Merging

## Slide 43: Multi-Mode Impact Weight:
Compute our previous metrics for each mode of operation separately
  reachability list in mode m
  : restorability rate in mode m
  : restoration demand in mode m
  impact weight in mode m
Add the impact weights of all the modes
  : multi-mode impact weight of flipflop f
Preliminaries
Single-mode
Multi-mode
Simulation Results
Algorithm
MMTS
Mode Merging
Reachability List
Restorability Rate
Restoration Demand
Impact Weight
…

## Slide 44: Simulation Setup
Simulation Setup
  Use MSRR to measure the restoration quality
  Also compared with an upper bound on MSRR
  Experimented with trace buffers of size 64 X 2K
Preliminaries
Single-mode
Multi-mode
Simulation Results
Algorithm
MMTS
Mode Merging

## Slide 45: Impact of Mode Merging
Bench | Suite | #FF | #Gates | M | 
S38584 | ISCAS’89 | 1166 | 10552 | 2 | 2
S35932 | ISCAS’89 | 1728 | 11032 | 4 | 2
b17 | IWLS’05 | 1317 | 33888 | 4 | 4
b18 | IWLS’05 | 3020 | 119762 | 2 | 2
dsp | IWLS’05 | 3605 | 54730 | 8 | 2
DMA | ISPD’12 | 2192 | 36556 | 8 | 4
des_perf | ISPD’12 | 8802 | 149066 | 2 | 2
Bench | Suite | #FF | #Gates | M | 
S38584 | ISCAS’89 | 1166 | 10552 | 2 | 2
S35932 | ISCAS’89 | 1728 | 11032 | 4 | 2
b17 | IWLS’05 | 1317 | 33888 | 4 | 4
b18 | IWLS’05 | 3020 | 119762 | 2 | 2
dsp | IWLS’05 | 3605 | 54730 | 8 | 2
DMA | ISPD’12 | 2192 | 36556 | 8 | 4
des_perf | ISPD’12 | 8802 | 149066 | 2 | 2
All benchmarks (excluding S38584 and S35932) are much larger compared to the ISCAS’89 used in prior works
In three benchmarks, the number of modes can be reduced by at least half and at most 4X
Preliminaries
Single-mode
Multi-mode
Simulation Results
Algorithm
MMTS
Mode Merging

## Slide 46: Impact of Mode Merging on MSRR and Runtime
MSRR Comparison
  MSRR for with/without mode merging are similar
Runtime Comparison
  Runtime reduction is significant
Chart: Runtime Comparison
| S35392 | dsp | DMA
W Merge | 1 | 1 | 1
W/O Merge | 1.5664 | 4.7193 | 1.7679
W Merge
W/O Merge
Chart: MSRR Comparison
| S35392 | dsp | DMA
W Merge | 60.6 | 36.2 | 46.5
W/O Merge | 62.8 | 39.4 | 47.7
Preliminaries
Single-mode
Multi-mode
Simulation Results
Algorithm
MMTS
Mode Merging

## Slide 47: Implemented Approaches
Comparison with other approaches including
  RATS: the single-mode procedure of Basu & Mishra [TVLSI’13]
  SimF: single-mode forward-greedy using X-Simulation Chatterjee et al. [ICCAD’11]
  HYBR: our proposed single-mode procedure
  HYBRM: simple extension of HYBR for multi-mode signal selection
    A forward greedy strategy which uses to identify top candidates
    Then uses X-Simulations to identify the next trace
  IteM: our proposed iterative multi-mode selection algorithm
  REF: upper bound on solution quality (MSRR) computed by
    Solving the SMTS for each mode separately by selecting different trace signals for each mode
    Adding the SRRs corresponding to the single mode solutions over all the modes
Preliminaries
Single-mode
Multi-mode
Simulation Results
Algorithm
MMTS
Mode Merging

## Slide 48: Comparison of MSRR
Bench | REF | RATS | HYBR | HYBRM | SimF | IteM
S38584 | 25.20 | 0.86 | 0.85 | 0.95 | 0.95 | 0.99
S35932 | 66.40 | 0.64 | 0.74 | 0.91 | 0.65 | 0.91
b17 | 7.90 | N/A | 0.62 | 0.76 | 0.58 | 0.94
b18 | 5.90 | N/A | 0.50 | 0.61 | 0.92 | 0.80
dsp | 42.80 | N/A | 0.41 | 0.37 | 0.88 | 0.92
DMA | 50.67 | 0.76 | 0.88 | 0.84 | 0.89 | 0.92
des_perf | 77.60 | N/A | 0.97 | 0.98 | 0.98 | 0.99
Average | 1.00 | N/A | 0.71 | 0.77 | 0.83 | 0.93
REF column reports an upper bound on MSRR and the remaining columns are normalized with respect to REF
IteM performs better than other methods
Preliminaries
Single-mode
Multi-mode
Simulation Results
Algorithm
MMTS
Mode Merging

## Slide 49: Comparison of Runtime
Bench | RATS | HYBR | HYBRM | SimF | IteM
S38584 | 0.1 | 2 | 4 | 19 | 13
S35932 | 0.1 | 2 | 5 | 14 | 15
b17 | > 24hrs | 1 | 4 | 19 | 24
b18 | > 24hrs | 4 | 119 | 2151 | 90
dsp | > 24hrs | 2 | 28 | 92 | 251
DMA | 5 | 7 | 38 | 99 | 125
des_perf | > 24hrs | 16 | 24 | 469 | 94
Runtime is reported in minutes
  RATS, although fast for the ISCAS’89 benchmarks, didn’t scale for the large benchmarks (took more than 24hrs)
RATS and SimF do not scale well over some benchmarks
The runtime of IteM is reasonable given the large size of the benchmarks comparable to SimF and HYBRM
Preliminaries
Single-mode
Multi-mode
Simulation Results
Algorithm
MMTS
Mode Merging

## Slide 50: Summary of MMTS
We proposed the multi-mode trace signal selection problem and algorithm
Experimental results showed that our algorithm performed better than various single-mode and multi-mode algorithms, with a high solution quality comparable to the reference case
Preliminaries
Single-mode
Multi-mode

## Slide 51: Conclusions
We proposed a hybrid SMTS algorithm
  Obtained the best solution quality with the best runtime
First to study the MMTS problem
  Showed that it achieved the best multi-mode restoration with reasonable runtime
Also proposed a procedure for automated identification of control signals
  They were fed into our single-mode and multi-mode trace signal selection problem
  Correctly identified same control signals as Ko et al [PhD Thesis]

## Slide 52
Thank You!

## Slide 53: References
K. Basu and P. Mishra. RATS: restoration-aware trace signal selection for post-silicon validation. In IEEE TVLSI, 2013
D. Chatterjee, C. McCarter, and V. Bertacco. Simulation-based signal selection for state restoration in silicon debug. In ICCAD, 2011
M. Li and A. Davoodi. A hybrid approach for fast and accurate trace signal selection for post-silicon debug. In DATE, 2013
H. F. Ko and N. Nicolici. Algorithms for state restoration and trace signal selection for data acquisition in silicon debug. In IEEE Trans. on CAD, 2009
X. Liu and Q. Xu. On signal selection for visibility enhancement in trace-based post-silicon validation. In IEEE Trans. on CAD, 2012
H. F. Ko. New algorithms and architectures for post-silicon validation. PhD thesis, McMaster University, 2009.
M. Paniccia, T. M. Eiles, V. R. M. Rao, and W. M. Yee. Novel optical probing technique for flip chip packaged microprocessors. In International Test Conference, pages 740–747, 1998

## Slide 54: Comparison with Forward-greedy Selection Strategy Based on Pure Simulation
Apply simulation on all untraced flipflops to select the one with the highest SRR. Traces are selected using forward-greedy selection strategy
Circuit | #Traces | Forward Greedy W Simulation | Ours | Improvement
S5378 | 8 | 13.5 | 13.6 | +0.7%
 | 16 | 7.9 | 8.0 | +1.3%
 | 32 | 4.2 | 4.2 | 0.0%
S9234 | 8 | 9.8 | 9.8 | 0.0%
 | 16 | 5.9 | 6.8 | +15.3%
 | 32 | 3.5 | 3.6 | +2.9%
S35932 | 8 | 59.3 | 61.4 | +3.5%
 | 16 | 37.4 | 38.3 | +2.4%
 | 32 | 22.3 | 23.4 | +4.9%
S38417 | 8 | 51.5 | 51.4 | -0.2%
 | 16 | 24.0 | 30.1 | +25.4%
 | 32 | 16.8 | 17.5 | +4.2%
S38584 | 8 | 25.1 | 24.0 | -4.4%
 | 16 | 20.7 | 18.5 | -10.6%
 | 32 | 18.0 | 17.5 | -2.8%
Avg. |  |  |  | +2.8%

## Slide 55: Impact of X-Simulation on SRR
The difference is without using simulation among the top candidates and simply picking the one with the highest impact weight as the next trace signal
Circuit | #Traces | Ours W/O Simulation | Ours | Improvement
S5378 | 8 | 13.4 | 13.6 | +1.5%
 | 16 | 7.9 | 8.0 | +1.3%
 | 32 | 4.0 | 4.2 | +5.0%
S9234 | 8 | 9.4 | 9.8 | +4.3%
 | 16 | 6.1 | 6.8 | +11.5%
 | 32 | 3.3 | 3.6 | +9.1%
S35932 | 8 | 31.6 | 61.4 | +94.3%
 | 16 | 18.9 | 38.3 | +102.6%
 | 32 | 11.3 | 23.4 | +107.1%
S38417 | 8 | 18.1 | 51.4 | +184.0%
 | 16 | 10.3 | 30.1 | +192.2%
 | 32 | 5.9 | 17.5 | +196.6%
S38584 | 8 | 18.3 | 24.0 | +31.1%
 | 16 | 14.8 | 18.5 | +25.0%
 | 32 | 10.7 | 17.5 | +63.6%
Avg. |  |  |  | +68.6%

## Slide 56: Impact of Island Flipflops on SRR
The difference is only without adding the island flipflops whenever 8 traces are selected
Circuit | #Traces | Ours W/O Islands | Ours | Improvement
S5378 | 8 | 12.5 | 13.6 | +8.8%
 | 16 | 7.8 | 8.0 | +2.6%
 | 32 | 4.1 | 4.2 | +2.4%
S9234 | 8 | 8.1 | 9.8 | +21.0%
 | 16 | 6.5 | 6.8 | +4.6%
 | 32 | 3.5 | 3.6 | +2.9%
S35932 | 8 | 61.4 | 61.4 | 0.0%
 | 16 | 38.3 | 38.3 | 0.0%
 | 32 | 23.4 | 23.4 | 0.0%
S38417 | 8 | 48.2 | 51.4 | +6.6%
 | 16 | 28.7 | 30.1 | +4.9%
 | 32 | 16.7 | 17.5 | +4.8%
S38584 | 8 | 23.9 | 24.0 | +0.4%
 | 16 | 18.5 | 18.5 | 0.0%
 | 32 | 17.5 | 17.5 | 0.0%
Avg. |  |  |  | +3.9%

## Slide 57: Correctly Identified Top Candidates
Ran on S38417
At each iteration, recorded the indexes of the top candidates identified using the impact weight metric
Then applied a variation in which the top candidates at each iteration are found using X-Simulation
Compared the two sets and reported the percentage of flipflops which are common, for the same number of top candidates
More than 90% of the top candidates are correctly identified

## Slide 58
Impact of Signal Correlation On The Accuracy of Metric Computation
Compute the “visibility” metric for the output pin of an AND gate
  Based on two input pins, each has
  But actual restored values for the two pins are interleaved
should actually be 0 but computed as 0.25

## Slide 59: Computation of “Restorability Rate”
  Based on X-Simulation for an observation window of n=64 cycles
    At each call of X-Simulation, the previously-restored signals and the trace signals selected from the current iteration are used to restore new signals
    Runtime complexity of the algorithm dominated by the 64 calls to X-Simulations
    However, the restorability rates of all the untraced flipflops are computed within one call of the algorithm
Alg: Restorability Rate
1:
2: for n = 1 to 64 do
3: =X-Simulation()
4: for each do
5:
6: end for
7: end for
8:
: restorability rate of flipflop f
: trace signals at cycle n
: the set of restored signals
Notes: Explain 64 cycles thing.
Explain the S_T^n.
Simulate initially for 64 random input pattern sets. Record the value of each cycle at internal nodes. Pre-processing step. If selected, just bring the value here.
Up to that round, it’s not yet the buffer bandwidth.
As the selection process proceeds,

## Slide 60: Comparison of SRR with Liu & Xu
Circuit | #Traces | Liu & Xu | Ours | Improvement
S35932 | 8 | 19.2 | 83.0 | +331.4%
 | 16 | 14.0 | 45.0 | +222.4%
 | 32 | 8.7 | 23.0 | +165.0%
S38417 | 8 | 64.0 | 96.0 | +50.0%
 | 16 | 38.1 | 67.0 | +75.7%
 | 32 | 21.1 | 44.0 | +108.9%
S38584 | 8 | 18.6 | 52.0 | +179.3%
 | 16 | 18.6 | 30.9 | +65.9%
 | 32 | 14.2 | 17.9 | +25.7%
Avg. |  |  |  | +136.0%
For S38584, “g35” is set to “1”
For S35932, “RESET” is set to “1” while “TM0” and “TM1” can randomly change
S38417 does not have any control signal

## Slide 61: Comparison of SRR with Ko & Nicolici
“-R” case every signal is randomly changed for benchmarks excluding S38417
“-D” case for S35932, average the 4 modes
Circuit | #Traces | Ko & Nicolici | Ours | Improvement
S38584-R | 8 | 127.2 | 160.3 | +26.0%
 | 16 | 65.6 | 84.1 | +28.3%
 | 32 | 37.4 | 43.0 | +15.2%
S35932-R | 8 | 254.9 | 256.0 | +0.5%
 | 16 | 127.8 | 128.8 | +0.8%
 | 32 | 64.6 | 64.7 | +0.2%
S38584-D | 8 | 19.0 | 83.3 | +338.5%
 | 16 | 10.6 | 45.1 | +327.5%
 | 32 | 6.3 | 23.2 | +267.3%
S35932-D | 8 | 41.5 | 62.8 | +51.5%
 | 16 | 39.3 | 42.3 | +7.7%
 | 32 | 24.8 | 27.7 | +11.8%
S38417 | 8 | 19.6 | 52.1 | +165.7%
 | 16 | 11.2 | 30.8 | +174.2%
 | 32 | 6.73 | 17.8 | +164.8%
Avg. |  |  |  | +105.3%

## Slide 62: Comparison of SRR with Basu & Mishra
“-R” case every signal is randomly changed for benchmarks excluding S38417
“-D” case is same as Liu & Xu
Circuit | #Traces | Basu & Mishra | Ours | Improvement
S38584-R | 8 | 155 | 156 | +0.6%
 | 16 | 82 | 83 | +1.2%
 | 32 | 42 | 42 | 0.0%
S35932-R | 8 | 188 | 192 | +2.1%
 | 16 | 96 | 99 | +3.1%
 | 32 | 50 | 52 | +4.0%
S38584-D | 8 | 78 | 83 | +6.4%
 | 16 | 40 | 45 | +12.5%
 | 32 | 20 | 23 | +15.0%
S35932-D | 8 | 95 | 96 | +1.1%
 | 16 | 60 | 67 | +11.7%
 | 32 | 35 | 44 | +25.7%
S38417 | 8 | 55 | 52 | -5.5%
 | 16 | 29 | 31 | +6.9%
 | 32 | 16 | 18 | +12.5%
Avg. |  |  |  | +6.5%

## Slide 63: Comparison of Runtime with Basu & Mishra
Runtime shown in seconds
Circuit | #Traces | Basu & Mishra | Ours | Basu & Mishra / Ours
S38584-R | 8 | 320 | 55 | 5.8
 | 16 | 341 | 70 | 4.9
 | 32 | 409 | 313 | 1.3
S35932-R | 8 | 336 | 43 | 7.8
 | 16 | 378 | 67 | 5.6
 | 32 | 411 | 110 | 3.7
S38584-D | 8 | 322 | 35 | 9.2
 | 16 | 354 | 55 | 6.4
 | 32 | 421 | 217 | 1.9
S35932-D | 8 | 345 | 41 | 8.4
 | 16 | 389 | 58 | 6.7
 | 32 | 441 | 97 | 4.5
S38417 | 8 | 529 | 116 | 4.6
 | 16 | 571 | 256 | 2.2
 | 32 | 649 | 443 | 1.5
Avg. |  |  |  | 4.98

## Slide 64: Experimental Results for Control Signal Identification
Circuit | #PIs | #Control Signals | %Candidates | Runtime(sec)
S38584 | 38 | 1 | 5.3% | 2.19
S35932 | 35 | 2 | 8.6% | 2.35
b17 | 37 | 2 | 16.2% | 0.76
b18 | 36 | 1 | 2.8% | 1.62
dsp | 586 | 3 | 0.9% | 8.49
dMA | 682 | 3 | 1.8% | 6.63
des_perf | 234 | 1 | 0.4% | 11.55
Avg. | 235 | 1.86 | 5.1% | 4.80

## Slide 65: Accelerating the Selection Process
Incremental update of the restoration map
  New signal values only restored at cycles which are previously unknown; already restored values remain unchanged
  Temporarily store the restoration map after a new trace is selected
  At each iteration, performed X-Simulation based on the value of new trace signals and the temporary restoration map; restoration effort is saved for already restored signal values
Parallel X-Simulation on multiple candidates
  Make multiple copies of the circuit, with each one attached to one set of candidate trace signals
  Apply X-Simulation to each set simultaneously
  After obtaining the SRR, reuse the memory of each copy and attach them to new candidate trace sets
  The idea of using extra “memory to trade for speed”

## Slide 66: Multi-Mode Metrics: Reachability List
f1
f3
f2
c
reachability list in mode m
  Defined for a specific mode m
  Example: