## Slide 1: Multi-Mode Trace Signal Selection for Post-Silicon Debug
Min Li and Azadeh Davoodi
Department of Electrical and Computer Engineering
University of Wisconsin-Madison
WISCAD Electronic Design Automation Lab http://wiscad.ece.wisc.edu/
Notes: Title?

## Slide 2: Outline
Preliminaries
  Overview of post-silicon debug (PSD) using trace buffers
  Review of restoration process and previous works
Introduction to restoration using control signals and operation modes
Motivation of multi-mode trace selection (MMTS)
An iterative MMTS algorithm
  New metrics for trace signal selection
  Mode merging and iterative selection process
Experimental results

## Slide 3: Post-Silicon Debug
Real-time operation of a few manufactured chips with real-world stimulus
Involves finding errors causing malfunctions
  Fix through multiple rounds of Silicon Stepping/Revision
Has become significantly time-consuming and expensive
  Tight Time-to-Market requirement
  Formal verification and simulation tools do not scale as technology scales
  Poor visibility inside the chip

## Slide 4: Debug using Trace Buffers
Use trace buffer technology
  Trigger an event in the CUD
  Real-time capture traces on a few selected state elements through on-chip buffer
  Extract and analyze
Reveals internal states at real-time operation
Off-chip state restoration
[Figure from Yang, et al DATE09]

## Slide 5: Trace Signal Selection Problem
Limitation
  Small trace buffer width (8~32 bits) and depth (1K~8K clock cycles)
  Limited on-chip white spaces
  Automated trace selection
  Need to select a subset of state elements to trace such that the visibility of internal signals is maximized
  Based on algorithms rather than hints and experiences

## Slide 6: Restoration Using Traced Signals
Forward
Propagation
Backward
Justification
f1
f2
f4
f5
f3
0
0
0
0
DFF\Cycle | 0 | 1 | 2 | 3 | 4
F1 | X | X | X | X | X
F2 | 0 | 1 | 1 | 0 | X
F3 | X | X | X | X | X
F4 | X | X | X | X | X
F5 | X | X | X | X | X
1 | 1 | 0 | X | X
X | 1 | 1 | X | X
X | 0 | X | X | 0
State Restoration Ratio (SRR):
# tot. FF restored
# tot. FF traced
e.g. in this example 11/4=2.75

## Slide 7: Control Signals and Modes
f1
f3
f2
c
control signal
Examples of control signals include signals for mode selection, scan enable, power gating and clock gating, encryption, etc.
control signals result up to number of modes
A single mode is defined as each control signal taking a constant value “0” or “1” throughout the debugging process
“Multi-mode” refers to the combination of all single modes

## Slide 8: Need to Consider Multiple Modes
 | 17.0 | 4.3
 | 14.3 | 8.2
 | 17.0 | 4.3
 | 14.3 | 8.2
    Case study of S38584
      For each solution evaluated the SRR for mode 0 and 1
Observations
  SRR of SMTS solution in each mode is higher in that mode
    For example is higher for solution of compared to
  Therefore solving SMTS for one mode may result in poor restoration in the other modes which may be a problem during the debug process since the operation mode when a bug occurs is not a-priori known
      Ran single mode trace selection (SMTS) procedure (of Li & Davoodi [DATE’13]) twice, for modes 0 and 1, to select two different sets of trace signals
      For each solution evaluated the SRR for mode 0 and 1

## Slide 9: Previous Works
Previous works give procedures for solving the trace selection problem for a single operation mode
  Ko & Nicolici [DATE’08]
  Liu & Xu [DATE’09]
  Prabhakar & Xiao [ATS’09]
  Basu & Mishra [VLSI’11]
  D. Chatterjee [ICCAD’11]: pure simulation with backward elimination
  Li & Davoodi [DATE’13]: a hybrid algorithm combining fast metric and accurate simulation
Two major drawbacks of applying single mode trace selection algorithms for multi-modes
  Traces selected for different modes may have little in common
  Traces selected for one mode may not be good for other modes

## Slide 10: Contributions
A new metric and problem definition when considering multiple modes
  Multi-mode State Restoration Ratio (MSRR)
  Multi-Mode Trace Selection problem (MMTS)
Algorithms for solving MMTS including
  A procedure to reduce the number of modes by merging the modes with “similar” restoration maps
  A procedure based on perturbing an initial single-mode optimized solution (selected from a suitable “start” mode) to improve the restorability over all the modes

## Slide 11: Multi-mode Trace Selection Problem
Multi-mode State Restoration Ratio (MSRR)
  Defined as summation of state restoration ratios (SRRs) of different modes obtained from a given set of selected trace signals
Multi-mode Trace Selection problem (MMTS)
  Given a trace buffer of size , and a set of control signals defining operating modes, the Multi-mode Trace Selection (MMTS) problem selects state elements, in order to maximize MSRR

## Slide 12: Mode Merging: Motivation
For S35932 we plotted four restoration maps when each of its four operation modes are set to the corresponding values (when no trace signal is selected yet)
In each restoration map
  Green pixel: gate restored to 0
  Black pixel: gate restored to 1
  Red pixel: unrestored gate
Observations
  Modes with similar restoration maps can be merged into a single mode
  In this case, modes 0 and 1 can be merged, so is modes 2 and 3c

## Slide 13: Mode Merging: Procedure
Consider any two modes and
Measure the number of restored gates ( and ) for each mode
?
Y
N
Merged the two modes (into one of the modes)
Count the number of common gates in and denoted by
Compute similarity ratio
Can’t merge the two modes

## Slide 14: MMTS Procedure: Metrics
reachability list in mode
  The set of state elements which can be restored solely by flipflop f when f takes value v (0 or 1) and control signals take constant values corresponding to mode m
  Example :
f1
f3
f2
c

## Slide 15: MMTS Procedure: Metrics
: restoration demand in mode m
  : restoration rate of flipflop i in mode m using the traces selected so far
  : rate that flipflop f takes value v in mode m
  Approximates how much of the restoration of flipflop i can be provided by flipflop f when f takes value v
  : how much more is needed for full restoration of i
  : how much f can offer to the restoration of i

## Slide 16: MMTS Procedure: Metrics
Impact Weight in mode m
The impact weight reflects how much flipflop f can contribute to restoring the remaining untraced elements in its reachability list
: Multi-mode impact weight of state element f
  Measures the contribution of f to MSRR if it is selected as a trace signal

## Slide 17: IteM: Iterative Multi-mode Trace Selection
Overview of our procedure:
Identify a suitable start mode minit
    For each mode compute a set representing the union of the reachability lists for all the flipflops in that mode, and then let the start mode to be the one which has the highest size for this set
Find an initial solution to maximize the SRR in mode minit
  Generated using Li & Davoodi [DATE’13]
Iteratively perturb the current solution for better multi-mode restoration
  Has a a non-greedy nature
  Is based on a gradually-increasing perturbation radius r within each iteration
  Specifically, at each iteration, up to R=3 number of trace signals in the current solution may be swapped
The process terminates upon observing no improvements in MSSR in 20 consecutive iterations

## Slide 18: IteM: Iterative Multi-mode Trace Selection
Swap r signals
r > R
?
DONE
Set swap to DET (deterministic);
radius r=1
START
Swap is DET ?
Set swap to
RAND
(random);
radius r=1
Accept
?
r++
N
N
Y
Y
N
Y
swap RAND
r=1 signal
Overview of swap for R trace signals:
Gradually increases the perturbation radius from r=1 to r=R
Uses a probabilistic acceptance criteria similar to simulated annealing to probabilistically accept the swaps when there is no improvement in MSRR

## Slide 19: IteM: Iterative Multi-mode Trace Selection
Overview of swap for r trace signals:
Consists of the following two basic steps:
  Eliminate r trace signals which are least promising
    Evaluate how much each currently-selected trace signal contributes to MSRR using simulation and eliminate r trace signals with the least contribution
    If the above deterministic elimination does not lead to improvement, randomly eliminate r trace signals
  Add r most promising trace signal
    Identify the top 3% of the flipflops with the highest value of the proposed multi-weight impact weight
    Use simulation to compute MSRR for the identified top flipflops and pick the one with the highest MSRR as the trace signal to add
    The above procedure is similar to Li & Davoodi [DATE’13]

## Slide 20: Experimental Results
Bench | #FF | #Gates | M |  | Suite
S38584 | 1166 | 10552 | 2 | 2 | ISCAS89
S35932 | 1728 | 11032 | 4 | 2 | ISCAS89
b17 | 1317 | 33888 | 4 | 4 | IWLS05
b18 | 3020 | 119762 | 2 | 2 | IWLS05
dsp | 3605 | 54730 | 8 | 2 | IWLS05
DMA | 2192 | 36556 | 8 | 4 | ISPD12
des_perf | 8802 | 149066 | 2 | 2 | ISPD12
Bench | #FF | #Gates | M |  | Suite
S38584 | 1166 | 10552 | 2 | 2 | ISCAS89
S35932 | 1728 | 11032 | 4 | 2 | ISCAS89
b17 | 1317 | 33888 | 4 | 4 | IWLS05
b18 | 3020 | 119762 | 2 | 2 | IWLS05
dsp | 3605 | 54730 | 8 | 2 | IWLS05
DMA | 2192 | 36556 | 8 | 4 | ISPD12
des_perf | 8802 | 149066 | 2 | 2 | ISPD12
All benchmarks (excluding S38584 and S35932) are much larger compared to the ISCAS’89 used in prior works
dsp has the maximum reduction in the number of modes, from 8 to 2, due to mode merging
Benchmark Information

## Slide 21: Implemented Approaches
RATS: implemented the single-mode procedure of Basu & Mishra [VLSI’11]
HYBR: single-mode procedure of Li & Davoodi [DATE’13] (our previous work)
SimF: single-mode forward-greedy selection based on simulation
HYBRM: simple extension of HYBR for multi-mode signal selection
IteM: the proposed iterative multi-mode selection procedure (this work)
REF: upper bound computed by adding the highest attainable SRR per mode
  Highest SRR/mode computed by solving the single-mode trace selection in that mode using various algorithms

## Slide 22: Comparison of MSRR
Bench | REF | RATS | HYBR | SimF | HYBRM | IteM
S38584 | 25.20 | 0.86 | 0.85 | 0.95 | 0.95 | 0.99
S35932 | 66.40 | 0.64 | 0.74 | 0.65 | 0.91 | 0.91
b17 | 7.90 | N/A | 0.62 | 0.58 | 0.76 | 0.94
b18 | 5.90 | N/A | 0.50 | 0.92 | 0.61 | 0.80
dsp | 42.80 | N/A | 0.41 | 0.88 | 0.37 | 0.92
DMA | 50.67 | 0.76 | 0.88 | 0.89 | 0.84 | 0.92
des_perf | 77.60 | N/A | 0.97 | 0.98 | 0.98 | 0.99
Average | 1.00 | N/A | 0.71 | 0.83 | 0.77 | 0.93
REF column reports MSRR and the remaining columns are normalized with respect to REF
Observations: IteM consistently performs better than other methods

## Slide 23: Comparison of Runtime
Bench | RATS | HYBR | SimF | HYBRM | IteM
S38584 | 0.1 | 2 | 19 | 4 | 13
S35932 | 0.1 | 2 | 14 | 5 | 15
b17 | < 24hrs | 1 | 19 | 4 | 24
b18 | < 24hrs | 4 | 2151 | 119 | 90
dsp | < 24hrs | 2 | 92 | 28 | 251
DMA | 5 | 7 | 99 | 38 | 125
des_perf | < 24hrs | 16 | 469 | 24 | 94
Runtime is reported in minutes
  RATS, although fast for the ISCAS89 benchmarks, didn’t scale for the large benchmarks (took more than 24hrs)
The runtime of IteM is reasonable given the large size of the benches and comparable with HYBRM which is based on simple extension of the very fast HYBR

## Slide 24: Conclusions
We proposed the multi-mode trace signal selection problem (MMTS)
We introduced a strategy to merge the modes with similar restoration maps
We proposed an algorithm to solve the problem based on iterative perturbation of an initial solution obtained from a single but suitable start mode
Experimental results showed that the iterative algorithm performs better than various single-mode or multi-mode algorithms, with a high solution quality comparable to the reference case

## Slide 25: References
K. Basu and P. Mishra. RATS: restoration-aware trace signal selection for post-silicon validation. In IEEE TVLSI, 2013
D. Chatterjee, C. McCarter, and V. Bertacco. Simulation-based signal selection for state restoration in silicon debug. In ICCAD, 2011
M. Li and A. Davoodi. A hybrid approach for fast and accurate trace signal selection for post-silicon debug. In DATE, 2013
H. F. Ko and N. Nicolici. Algorithms for state restoration and trace signal selection for data acquisition in silicon debug. In IEEE Trans. On CAD, 2009
X. Liu and Q. Xu. On signal selection for visibility enhancement in trace-based post-silicon validation. In IEEE Trans. on CAD, 2012

## Slide 26
Thank You!

## Slide 27: Experimental Results
Chart: Runtime Comparison
| S35392 | dsp | DMA
W Merge | 1 | 1 | 1
W/O Merge | 1.5664 | 4.7193 | 1.7679
W Merge
W/O Merge
Comparison of Merged/Unmerged Cases
Apply the iterative algorithm on the three benches having mode reduction (merged)
For “W Merge” case, randomly pick one mode to represent the modes merged
For MSRR comparison, raw numbers are shown (without normalization). For runtime comparison, results of the “W/O Merge” case are normalized to “W Merge”
Mode merging can significantly reduce the runtime while obtaining a comparable solution quality
Chart: MSRR Comparison
| S35392 | dsp | DMA
W Merge | 60.6 | 36.2 | 46.5
W/O Merge | 62.8 | 39.4 | 47.7